1. How to save the user phone number (total 3002 users)

a. Admin phone number setup

Insert the SIM card(called No. A) to the controller, and turn on it, do not operate until the blue led flash regularly (means the signal good).

1)Keep pressing RESET button for 3 seconds, Blue LED indicator light on, call with admin phone(called Admin) to No. A in 10 minutes. If save successfully,it will hang off the call automatically and send SMS to Admin (Save Admin OK)

Note:

(1) To change the admin number, just do same operation above again,the new admin number will be add,and the old one will be remove.

(2) If no phone number to be the admin in 10 minutes, it will exit from setting status automatically.

(3) Only admin number can be add by this way .

- To add/change the admin number,send SMS:

Admin Password+admin+Mobile Number+#

Eg:8888Admin1234567890#

（the default admin password is 8888）

b. Save other 3001 users numbers

- Saving Numbers by calling:

Admin send SMS :normal password+ADD ON,

eg:1234ADD ON to No. A,and will get a reply SMS: ADD ON

The other users can call the No. A in 30 minutes to be the users of the controller.It will hang off the call automatically and reply a SMS ADD  ********  OK to users.

Note:

(1)if no number call in in 30 mins,the state of number storage will automatic shutdown.

(2)In this mode,users can not do other operation.

Admin send SMS:normal password+ADD OFF,

eg:1234ADD OFF to No. A to stop saving number. and will get a reply SMS: ADD OFF

2)Saving numbers by SMS:

Admin send SMS : normal password+ AD+number 1+*+number2+*+…+ #  to No. A,and will receive a reply SMS ADD OK for confirmation.

Note: the Admin can save maximum 5 numbers in 1 SMS.

Eg: 1234AD1380013800#

1234AD1380013800*1380018001*1380013802*1380013803*1380013804#

2. How to Delete User Number

- Delete specified user number

Admin send SMS : Normal password+ DD+number 1+*+number2+*+…+ #  to No. A,and will receive a reply SMS Delete OK for confirmation.

Note: the Admin can delete maximum 6 numbers in 1 SMS.

Eg: 1234DD1234567891*1234567892*1234567893#

- Delete user automatically after it sending specific commands

Users Send SMS:Admin Password+Number+User Number+”*”+Command Number(max 250)+”#”

Eg:1234Number1234567890*012#

After the number 1234567890 send or call 12 command to control the relay,it will be deleted automatically.

- Delete all user number

Admin send SMS 1234FD  to No. A.

After operation successfully Admin will receive a SMS FD OK for confirmation

3. How to Change Password by SMS

1) Change the normal password:

Send SMS to No. A(only available for Admin): old passwords (4 digits)+CP +new password

Example: The default password is 1234, if you want to set 4321 as the new password,

Send SMS:

1234CP4321

After operation successfully, the Admin will receive a SMS for confirmation

CP:4321

2) Change the admin password:

send SMS (available for any number):Old Password+PASSWORD+New Password

Eg:send 8888PASSWORD9999,it will reply:set ok.

4. Setting Require

1) To check the Free Memory, normal password, and relay output mode:

(available by any user)

send SMS:CHK

it will reply SMS:

Mode A

Password: 1234

Free Memory :1234

2)To check admin password(only available by admin number)

send SMS:CHKA

it will reply SMS:

Mode A

Password: 1234

Admin Password:8888

Free Memory :1234

5. Confirmation Message Limitation

Generally,the controller will not send confirmation SMS when be called by users.

1) Allow specific users receive the confirmation SMS :

Users send SMS:

Admin Number+SMON+NUMBER1+”*”+NUMBER2+”*”+....NUMBER6+”#”

(max 6 numbers in 1 SMS)

Eg:8888SMON123456781*123456782*123456783*123456784*123456785*123456786#

2) Not allow specific users receive the confirmation SMS :

Users send SMS:

Admin Number+SMOFF+NUMBER1+”*”+NUMBER2+”*”+....NUMBER6+”#”

(max 6 numbers in 1 SMS)

Eg:8888SMOFF123456781*123456782*123456783*123456784*123456785*123456786#

6. Output Mode Setup

The controller has 2 relay output, 4 output modes,the default mode is mode A.Only admin can change the mode.

Mode A:only the first relay output works.When the users call No. A,it will hang off the call automatically.The first relay will on in 3 seconds and off automatically.

Also users can send SMS: 1234CALL to turn on/off the relay.

The relay time can be set up from 1-86400 seconds by send the SMS to No. A::

normal password+MA+seconds+ “#”

e.g.:1234MA86400#

If allow the sms confirmation, when activate the relay,the reply SMS is: "OUT1 ON  OUT2 OFF” or  "OUT1 OFF  OUT2 ON”

when the first relay is on ,the controller will check the output 1 after the specified time ,if it’s in the low level,the unit will send SMS to specified numbers:GATE STILL OPEN.

Meantime, the second relay will on and then off after specified time.(same with the time of relay1)

if the output 1 is is high level,it will not send SMS.

Mode B:only the first relay output works.When the user call No. A over 10 seconds,it will hang off the call automatically.The first relay will open(could not off automatically).When the user call No. A again,it will hang off the call automatically in 2 seconds and the relay will off.

Also users can send SMS: 1234CALL to turn on/off the relay.

send SMS: normal password+MB+0(or 1) + “#”.

e.g.:1234MB1#

0 :the controller will not inform the user who call in when relay on/off.

1: the controller will inform the user who call in when relay on/off.

If allow the sms confirmation,when activate the relay,the reply SMS is: OUT1 ON

Mode C: two relay output,when the user call No. A over 10 seconds,it will hang off the call automatically.The first relay will on and off in the preset time.

when the user call it again,it will hang off the call automatically.The second relay will on and off in the preset time.

Also users can send SMS: 1234CALL to turn on/off the relay.

The relay time can be set up from 1-86400 seconds by send the SMS to No. A:

normal password+MC+seconds+ “#”

e.g.:1234MC00088#

If user is allow to receive sms confirmation,he will received sms: "OUT1 ON  OUT2 OFF” or  "OUT1 OFF  OUT2 ON”

Mode D: two relay output,when the user call No. A over 5 seconds,it will hang off the call automatically.The first relay will open(could not off automatically),and the second relay will off.

when the user call it again,it will hang off the call automatically.The first relay will off,and the second relay will on.

Also users can send SMS: 1234CALL to turn on/off the relay.

send SMS to No. A:

normal password+MD+0(or 1)+ “#”.

e.g.:1234MD1#

0 :the controller will not inform the user who call in when relay on/off.

1: the controller will inform the user who call in when relay on/off.

If allow the sms confirmation, when activate the relay,the reply SMS is: "OUT1 ON  OUT2 OFF” or  "OUT1 OFF  OUT2 ON”

Note:To close both relays, users send SMS:1234OFF12# ,it will reply OFF12 OK.

7. Wired connection function

1) When the input1(or 2) is triggered ,the relay 1(or 2 ) will on or delay off,and the relay state will be sent to the specified users,such us:

TRIGGER 1
RELAY1 ON
RELAY2 OFF

Admin can set relay time first by sms:

1234DEAY00030#

The relay will off after 30 seconds(max 99999 seconds).

.Users can control the relays separately by SMS:

- 1234ON1#

Reply:OUT 1 ON

(relay 1 will on and off in 3 seconds, the default time is 3 seconds)

- 2)1234OFF1#

Reply:OUT 1 OFF

( relay 1 will off)

- 1234ON2#

Reply:OUT 2 ON

( relay 2 will on and off in 3 seconds, the default time is 3 seconds)

- 1234OFF2#

Reply:OUT 2 OFF

(relay 2 will off)

- 1234OFF12#

Reply:OFF 12 OK

(both relay will off)

2) Admin to turn on/off the SMS confirmation for the wired connection,send SMS:1234ME0(or 1)#

- close ,1-open,the default setting  is 0)

Note:the users which are allowed or not allowed to receive sms confirmation is same as the first 5 number of the Point 5.

8. SIM card testing

User send SMS TEST to No. A for checking the SIM status, If received a SMS TEST, means SIM card working normally. Without SMS reply means SIM card doesn’t working.

9. Reset

Keep pressing RESET button and turn on it for about 15 seconds, Three LED indicator will flash 3 times. It means the controller has been reset to default setting.