HD DV WRISTWATCH

USER’S MANUAL

- Profile

This product is the first wristwatch with HD digital function,camera function,Motion Detector,PC Camera.It looks lovely,but a useful wristewatch.The lovely designed wristwatch is easy to operate.

- Before use please read the following：

    - This product is with the anti-waterproof function.According to the structure and process of anti-waterproof,we design and product it.

      - The nut,A：MIC1 and the nut,B:MIC2 are microphone hole nut,the height of them are same.

      - The nut A,MIC1 is with a hole in the center of the nut(the following picture),it is for transmite the sound.If the environment permit,please use this nut.When you take the video,the equipment also can record the sound.

      - The nut,B：MIC2 is without the hole,but it is with a rubber fitting inside which can anti-water,When it is in the humidity or dust environment,please use this nut.But when you use this nut,the equipment can not record the sound.

      - Please tighten the nuts when you use the equipment.

      - Before use the nut,please check if the rubber is inside of the nut.If not,please change the new one.

Picture1

THE NUT STRUCTURE SHOWED AS FOLLOWING PICTURE:

Picture2

The following Spare Parts introduction showed as the picture3

- Spare Parts：

  - Interface：USB（No.1），is for connecting pc or recharger.

  - Microphone：Microphone（No.2），Taking sound；Lens（No.3）.

  - Operating Key（No.4）is for on/off,,starting or stoping taking video；

  - Time reset：Reset（No.5）is for resetting the time.

  - Camera/Motion Detector Key（No.6）is for starting or stopping taking camera,Motion Detector。

  - Indicator：No.7 is the status indicator.When the equipment is taking video,the red light is burning.But the blue light is for camera.When the equipment is recording sound,the red light and the red one are burning together.

- STRUCTURE

Picture3

1、USB   2、MICROPHONE   3、LENS   4、ON,OFF/VIDEO KEY

5、TIME RESET  6、CAMERA/MOTION DETECTOR KEY  7、STATUS INDICATOR

    - OPERATION

- On：Press the key,No.4 for about two seonds,the red light and bule light will be burn together,when the red one is off and blue one is burning.The equipment is standby.

- Off：In the condition of standby or video,press the key,No.4 for two secondes, the equipment will be off after the red light is shining for three time.The equipment will be off after three minutes in the condition of standby if it does not receive any order.

- Video:In the condition of standby,after you press the key No.4,the blue light will be off after shining three time.It means the equipment is in the condition of video.In the condition of video,press the key,No.4,the equipment will store the file and enter into the standby condition.

- Camera:In the condition of standby,after you press the key,No.6 for one time.The red light will shine one time.It means it takes one picture and stores it as JPG file.

- Motion Detector:In the condition of standby,please press the key,No.6 for two seconds,the red ligth  will shine three times.It means it enters into motion detector mode.If there is any object is moving in the working area,the equipment will take video automatically,and it will store the file every three minuts.If the object stops moving,the equipment will stop taking video within three minutes.

- PC Camera:If it is the first time for you to use it in the computure,you need to install the driving progarmme.After you install the programe,you can connect the equipment and PC.But please remember when you connet it to the pc,please press the key,No.6 at the same time,after you connnet it to the pc,you can releas it.

- Reset:If the system halted,please press the key,No.6 firstly,then press the key,No.4.It can reset the equipment.When you press the on/off,please do not release the camear key.

- Mobile Disc:When it is in the condition of the off or standby status,you can connect the equipment and the PC.The mobile disc sign will show in the screen.

- Charge:After you connect the equipment and PC or charger,the red light will shine slowly.After it is full,the red light will burn.

- Time Reset:When you watch the video,you can find there is the time showing in the video.But it can be changed as following:

  - Building Time File:

      - First step:Turn Off the equipment;Second Step:Connect the equipment and PC;Third Step:Open the mobile disc;Fourth:Building a file named time.txt.

Open the file,time.txt,input the time you want to show.The show mode should be

              - YYYY.MM.DD HH.MM.SS Y

              - YYYY.MM.DD HH.MM.SS N

If you want to show the time with the video together,please choose Y,but if you don’t want to show the time,please choose N.

  - After you confirm you have copied this file in the mobile disc,you can disconnect and turn on the equipment.

- FAQ

    - If the capacity is full,the blue light and red light will shine for about five seconds and power off after it stores the file.

    - If the power is low, the equipment will store the file and power off after the blue light and red light will be shine alternately for about five seconds.

    - If the equipment stop responding for unknown reason or wrong operating,please press the mode key and operating key together to reset.

- Parameter

| Iterm | Parameter |
| --- | --- |
| GVI | AVI |
| Video Coding | M-JPEG |
| Resolution | 640*480 |
| Player Software | Operating systems or mainstream movie playback software |
| Picture Format | JPG |
| Image Scaling | 4:3 |
| Suppot System | Windows me/2000/xp/2003/vista；Mac os 10.4；Linux； |
| VOL | DC-5V |
| Interface-type | Mini 4 Pin USB |
| Memory Card Format | Nand flash |
| Battery | High-capacity polymer lithium battery |

- Notice

  - Work place:It is only for legal place.

  - Battery:You need to charge it after it does not work for long time.

  - File safty:It is not the professional memory card,so it can not instead of professional memory card completely.you need to keep back-up.

  - Video quality:It is not the professinal video equipment,so it can not instead of professional Video Equipment completely.

  - Working tempreture: 0—45°C,it is better to use in the room tempreture.

  - Working humidity:20%-80%,it is with waterproof function.Before you enter into the waterproof status,do not put it into water or humidy place.

  - Illuminance: Please to use it in the luminous place.

  - Cleanliness:it is better not to use it in the dust place.

  - Other iterms:It can not use in the high magnetic fields , uniform electric field.It can not be striked,quick hardly.

  - Notice:Please contact the local selleres if you need any other more inforamtion or help.

# Text boxes

PICTURE IS ONLY FOR REFERNCE